# Sinclair QL Printer

# Replacement Manual

# _CONTENTS_____________________________________________

MAIN FUNCTIONS	1

SWITCHES AND LAMPS	2

CONNECTING TO THE   COMPUTER	4

INTRODUCTION TO   PRINTOUT	5

PAPER   LOADING	7

RIBBON	INSTALLATION/REMOVAL		14

HEAD POSITION ADJUSTMENT		16

MARGIN SETTING BY SWITCHES		17

SELF TEST   PRINTING FUNCTION		18

AUTOMATIC PRINTING FUNCTION		18

AUTOMATIC PAPER LOADING FUNCTION		18

HEXADECIMAL	DUMP   LIST FUNCTION		19

PRINT MODE   FLOWCHART		20

CONTROL	CODE EXPLANATION'S		21

DIP   SWITCH SETTING		56

SERIAL   INTERFACE		56

CHARACTERSET TABLE		57

TROUBLESHOOTING		58

CAUTIONS FOR USE		59

APPENDIX	A (Specifications)		60

APPENDIX	B (Character Category Priority Table)		61

APPENDIX	C (Character Category Specifications)		66

APPENDIX	D (Control Code Summary)		67

# _MAIN FUNCTIONS_______________________________________

- Paper out detection function

Paper detection function determines whether paper is out or not.

- A variety of character fonts are possible including High Quality (N.L.Q.), Proportional and Graphic printing.

- Form feed function:  possible by using the switch or the corresponding   command.

- Self Test printing

- Automatic printing

- Double Width Character mode

- Bold Character mode

- Double Strike Character mode

- Italic Cursive Character mode

- Buzzer function

- Internal RAM error detection function

- Hexadecimal dump list function

- Automatic paper loading function

- Margin designating function (both sides): by using the switches or the corresponding command.

- Automatic paper feeding out function

- When a paper out is detected,  the paper automatically advances by three more inches for easier paper removal.

# _SWITCHES AND LAMPS_________________________________

A.    POWER switch

Turns the printer ON/OFF.

B.    ON-LINE switch

Puts the printer into the ON-LINE/OFF-LINE state. Pressing this switch puts

the   printer into the opposite state. In the OFF-LINE state a BUSY signal is

output. The head moves to the home position when the printer goes from the

OFF-LINE state to the ON-LINE state.

C.   NLQ switch (Near Letter Quality)

(Valid only while in the OFF-LINE state) Selects the High Quality or

Standard mode. Pressing this switch selects the other print mode.

If the High Quality mode is selected the lamp is on. If

the Standard mode is selected the lamp is off.

D.  LF switch (Line Feed)

(Valid only while in the OFF-LINE state)

Each time this switch is pressed a 1/6 inch line feed is performed.

E. FF switch (Form Feed)

(Valid only while in the OFF-LINE state)

Pressing this switch results in a form feed. The length of each page is determined by the DIP switches or is command designated.

F.	POWER lamp (green)

Is on while the power is on.

G. ON-LINE lamp (green)

Is on while in the ON-LINE state (capable of receiving data), Is off while in the OFF-LINE state. If in the margin set mode it flickers at a rate of 0.3 seconds.

H. NLQ lamp (green)

Is on while in High Quality mode. Is off while in the Standard mode.

I.	P.  OUT  lamp  (red)

Is on if paper out is detected. In this case the printer enters the OFF-LINE state   and outputs a busy signal. The buzzer also sounds for 1 second.  If paper  is inserted and the ON-LINE switch is pressed this state is terminated.

While in the error state the lamp flickers.

# _CONNECTING TO THE COMPUTER_________________________

Follow the instructions below to connect the printer to the computer.

1.  Check that the monitor, the  printer and the computer are all switched off.

(: POWER for the power supply unit

(: RGB for a monitor

(: SER1 for the printer

2.  Connect the printer to the computer by the attached cable as shown above.

3.  Apply power to the printer, the monitor and the computer in this order.  When power is applied to the printer,   the print head makes one movement.

Note

Please remember not to connect the power supply lead to the computer until all other leads and peripherals have been connected. Always connect the power supply lead to the computer last of all.

4.   Install the ribbon cassette and set paper in the printer. Refer to "PAPER LOADING" and "RIBBON  INSTALLATION/REMOVAL"  to set them properly.

Note

After setting paper, make sure that the ON-LINE lamp is lit. If it is on, the printer is ready to receive data  from the computer.

_INTRODUCTION TO PRINT OUT___________________________

First, press the  F1  or  F2  key to select a screen you prefer.

Try typing in the program below and running it.

10 OPEN #3,ser   ENTER

20 PRINT #3,”I HAVE A PRINTER.”   ENTER

30 PRINT #3,”A VERY NICE PRINTER.”\\   ENTER

40 LIST #3   ENTER

50 CLOSE #3   ENTER

RUN   ENTER

The printout will be:

I HAVE A PRINTER.

A VERY NICE PRINTER.

10 OPEN #3,ser

20 PRINT #3,”I HAVE A PRINTER.”

30 PRINT #3,”A VERY NICE PRINTER.”\\

40 LIST #3

50 CLOSE #3

Each line of the program is explained as follows.

10 OPEN #3, ser

The OPEN command initialises a device and activates it for use. When a device is activated, a channel is opened and linked to the device. To correctly open a channel, device basic information must be supplied to initialise the device driver. #3 designates channel number 3, ser selects the SER1 port and its default setting is 8-bit no parity with handshake. The printer can receive only this default setting.

20 PRINT #3,”I HAVE A PRINTER.”

“I HAVE A PRINTER.” followed by a New Line code, 10 in decimal number, is now sent to the printer.

30 PRINT #3,”A VERY NICE PRINTER.”\\

40 LIST #3

The command allows the program stored in the computer to be listed on the printer.

50 CLOSE #3

The CLOSE command closes the serial channel for the printer. In thi scase it is channel 3 that is deactivated.

# _PAPER LOADING________________________________________

A.   Cut Sheet Paper

Remove the tractor unit when using friction feed for the cut sheet paper.

- Open the printer cover.

Fig.  1

- Hold the paper rack upright and insert it to the two supporters on both sides. Insert the folding leg into the hole located on the top of the case.

Fig. 2

3. Slide the paper guide right to the extreme right.

4.  Position the cut sheet paper at the extreme left of the paper rack as shown below.

Fig.3

5.  Slide the right paper guide to the left to match the paper width.

6.  Apply power to the printer.

7. The paper automatically advances to the TOF position if the paper loading knob is turned counter-clockwise.

TOF stands for Top Of Form.

Fig. 4

8. Turn the paper loading knob clockwise to set the paper bail.

9. Close the printer cover.

NOTE 1: If you wish to shift the loaded paper to the right or to the left, remove the paper by the paperfeed knob and repeat the process from step 3.

NOTE 2: If a cut sheet is positioned at the leftmost side of the paper rack, printing starts at a position one inch away from the left edge of a form.

Fig. 5

NOTE 3: The position of the paper guide, which has been installed at the leftmost end of the paper rack when shipped, can be adjusted by pulling it upwards. This will remove it from the paper rack. The user is then able to position it at any desired location.

Fig. 6

NOTE 4: When using the paper loading knob to automatically set a form, the ribbon at the print head may slightly be raised. But the user does not have to manually reset the ribbon because it automatically returns to its normal position before printing is performed. Therefore, printing is not affected at all by the ribbon raised.

NOTE 5:

Reference:  The paper out detection switch is located at a position about 6 centimeters away from the left edge of the platen. The left edge of a cust sheet of paper should cover the switch to avoid the paper out condition.

B. Continuous Forms

Fig.7 Paper feed path

- Remove the paper rack and the printer cover.

Make sure the power is turned OFF.

- Turn the paper loading knob counter-clockwise to move the paper bail toward the front.

- Install the tractor unit on the top of the platen in the following process.

( Insert the front hook of the tractor unit into the hole on both sides.

( Push down the rear of the tractor to fit the back hook securely.

Fig. 8

- Feed the paper into the printer from the back and then turn the paperfeed knob in a clockwise direction until it appears between the platen and the printhead.

Fig.  9

- Open the tractor covers on the left and right.

- Adjust the tractors such that the distance between them matches the holes in the paper.

- With the holes along both sides of the paper matched up with the paper feed pins on the left and   right tractors, close the tractor covers.

- Turn the paper loading knob clockwise to set the paper bail to the platen side.

NOTE: This is important to be done because the friction roller below the platen is released so that paper is free to be advanced by the tractors only.  Failure to do so may cause paper jamming.

Fig.  10

- Set the paper rack and the printer cover.

- Turn the power switch ON.

C. Top of Page Setting

- Cut sheet

- Paper out at power-on

If paper is input by the automatic paper loading function, printing is initiated 1 inch from the top.

This 1 inch worth of paper feed is stored within the printer’s memory.

- Paper already inserted at power-on.

The position of the paper in front of the print head at the time of power on is to become the top of form.

If cut sheets are to be used make sure that the print head is 1 inch from the top of the sheet.

- Continuous Form

- Paper already inserted at power-on.

The position of the paper in front of the print head at the time of power-on is to become the top of form position.

- To start printing at the perforationm adjust the paper using the paperfeed knob so that the perforation is located right above the printhead.

One of the followign steps is to then be taken.

- Turn the power on once again.

- Perform an   ESC   @   command.

- Perform an   ESC    C   command.

_RIBBON INSTALLATION/REMOVAL________________________

Installation

- Turn the ribbon feed knob in the direction of the arrow to remove slack in the ribbon

Fig. 11

- Insert the ribbon in-between the ribbon mask and the print head, and position the cassette so that the ribbon feed shaft is inserted into the hole under the ribbon feed knob.

NOTE: It is easier to insert the ribbon when the printhead is at the home position (extreme left).

Fig.  12

- Press on both sides of the cassette.

Fig. 13

- Twist the ribbon feed knob of the cassette to tighten the ribbon. Make sure that the ribbon is properly positioned in front of the printhead.

Removal

Hold the fin of the cassette and pull it up to remove.

Fig. 14

_HEAD POSITION ADJUSTMENT___________________________

The  print head position  can be adjusted  using the head adjustment  lever located inside of the printer on the rightband  side.

Position is suitable for one-part general paper.  The printer is shipped with the lever set to position (.

When using three-part  paper, it is recommended  that the lever be set to position ( or (.

_MARGIN SETTING BY SWITCHES__________________________

    - Margin mode switch (the M. MODE switch)

If this switch is pressed for more than 1 second in the ON-LINE state, the printer enters the right/left margin set mode. At this time the ON-LINE lamp will turn off and on every 0.3 seconds.

If pressed again, the printer will return to the ON-LINE state.

    - RIGHT switch

(Valid only while in the margin set mode)

By pressing this switch the print head moves to the right of its present position. The margin position is located at the center of the print head.

    - LEFT switch

(Valid only while in the margin set mode)

By pressing this switch the print head moves to the left of its present position. The margin position is located at the center of the print head.

    - Margin set switch (the M. SET switch)

(Valid only while in the margin set mode)

Pressing this switch sets the margin positions.

The margins are set from left to right.

The printer returns to the ON-LINE state as soon as the right margin is set.

If only the left margin is to be set, after setting the left margin, press the margin mode switch (the M. MODE switch). If only the right margin is to be set, it must be performed after setting the left margin.

The minimum margin setting possible is 1 PICA Double Width Character	worth. After the margin is set the buzzer sounds for approximately 0.1 second.

_SELF TEST PRINTING FUNCTlON__________________________

If the LF or NLQ switch is pressed during power-on a pattern is printed repeatedly. If the LF switch is pressed	 during power-on the self test printing is performed	in Standard Character	mode.	If the NLQ switch is pressed during power-on the self test printing is performed in High Quality Character mode.

The printer is in the OFF-LINE state while performing the self test printing function.

To stop the self test printing the ON-LINE switch is to be pressed.

At this time the ON-LINE lamp turns on.

During the self test printing,	if a paper out is detected the self test printing is terminated. The self test printing does not start in the paper out state.

_AUTOMATIC PRINTING FUNCTION_________________________

During the input process of character	data (excluding graphic data). if the amount of data exceeds	 1 line worth of characters, a printing and line feed is performed.

During	the input of graphic data, if the data exceeds	1 line, printing is performed without a line feed. The graphic data that exceeds 1 line is ignored.

_AUTOMATIC PAPER LOADING FUNCTION___________________

At paper out, if a form is inserted into the form entrance and the paper loading knob is turned counter-clockwise, the form is automatically inserted into the printer.

The distance from the top of the form to the first line printed is l inch. After loading, the paper loading knob is to be turned clockwise.

_HEXADECIMAL DUMP LIST FUNCTlON_____________________

This function is very useful if you want to check what codes the printer actually receives from the computer using various output commands.

The data that is input is printed in 2-digit hexadecimal numbers. This function can be set by pressing the FF switch during power-on. After printing a hexadecimal digit 2 characters worth of space is left open. This allows 16 pairs of data per line to be printed.

Printing is initiated after 16 pairs of data is input. If the input data is less than 16 pairs, pressing the ON-LINE switch will print the input data. After this printing is done the OFF-LINE state is set. Pressing the ON-LINE switch once more sets the hexadecimal dump function. The characters to be printed is set to Pica Character mode. High Quality Character mode can be set by pressing the NLQ switch in the OFF-LINE state.

The hexadecimal dump list function can be terminated by turning the printer off then on once again.

_PRINT MODE FLOWCHART________________________________

When the power is applied to the printer, the default mode automatically set is Pica character mode.

To print Italic characters, forst output the   ESC  4   command by typing:

PRINT #3,CHR$(27);”4”;

See the  ESC 4  command on page 28 for further details.

In print mode the following priorities exist:

- Elite > Proportional > Bold > Condensed > Pica

- Superscript/Subscript > High Quality > Double Strike

For greater detail refer to the character Category Priority Table.

The  ESC  !  command clears character modes specified thus far and sets modes according to its designation.

_CONTROL CODE EXPLANATIONS________________________

In this chapter,	 all the control commands are explained in detail. A square containing a symbol indicates one byte of control commands.

Then follows the actual code in Hexadecimal and Decimal numbers.

(1)  Print Command

1.   CR  				(OD) Hex (13) Decimal

Input of this code initiates printing. A line feed is not performed after printing. If print data is input or if the input data is all space code the print head does not move. The print data that is input after the CR command is printed from the left margin.

After this command is executed, the  SO  or  ESC   SO  Double Width mode is terminated.

If you run the listed program	below, you can get the printed sample.

}     Printed sample

10 OPEN #3,SER                        }

20 REMark CARRIAGE RETURN             }

30 PRINT #3,”PROGRAM ONE”;CHR$(13);   } Program list

40 PRINT #3,"PROGRAM TWO"\\\\ .       }

50 LIST #3                            }

60 CLOSE #3                           }

- NL                         		(OA) H  (l0) D

Input of this code imnates printing and performs a line feed after printing.	the amount of line feed is set by the line feed pitch command. If the print data is not input or if the input data is all space code only a line feed is performed. The print data that is input after this command is printed from the left margin.

After this command is performed, the  SO  or  ESC   SO  Double Width mode is terminated.

10 OPEN #3,SER

20 REMark LINE FEED

30 PRINT #3,"PROGRAM ONE";CHR$(10);

40 PRINT #3,"PROGRAM TWO"\\\\

50 LIST #3

60 CLOSE #3

- FF  				(0C) H   (12) D

Input of this code initiates printing and performs a form feed after printing. The form feed value (1 page length) can be selected from 2 choices by the DIP switches1-3 at power-on. This value can be altered by the   ESC   C  command.

After this command the  SO  or  ESC   SO  Double Width mode is terminated.

PROGRAM ONE

PROGRAM 2

PROGRAM THREE

11 inches

PROGRAM 4

10 OPEN #3,SER

20 REMark FORM FEED

30 PRINT #3,”PROGRAM ONE”\

40 PRINT #3,”   PROGRAM TWO”\

50 PRINT #3,”   PROGRAM 3”;CHR$(12);

60 PRINT #3,”PROGRAM FOUR”\\\\

70 LIST #3

80 CLOSE #3

- VT   				(0B) H  (11) D

This command forms the same function as the  NL  command.

10 OPEN #3,SER

20 REMark VERTICAL TAB

30 PRINT #3,”PROGRAM ONE”;CHR$(11);

40 PRINT #3,”PROGRAM TWO”\\\\

50 LIST #3

60 CLOSE #3

- ESC   J   n 			(1B, 4A, n) H   (27, 74, n) D

n is an 8-bit binary code   0 <= n <= 255

Input of this code initiates printing and performs an n/216 inch linefeed after printing. The amount of line feed is not stored in the printer.  After performing this command printing starts at the beginning of the line.  When n = 0, printing without a line feed is performed.

10 OPEN #3,SER

20 REMARK n/216 INCHES LINE FEED

30 PRINT #3,”PROGRAM ONE”;CHR$(27);”J”;CHR$(27);

40 PRINT #3,”PROGRAM TWO”\\\

50 LIST #3

60 CLOSE #3

(2) Character Mode Designation

- ESC   P   				(1B, 50) H  (27, 80) D

Input of this command terminates the Elite Print mode.

10 OPEN #3,SER

20 REMark ELITE CHARACTER

30 PRINT #3,”PICA CHARACTER 1”\

40 PRINT #3,CHR$(27);’M’;

50 PRINT #3,”ELITE CHARACTER”\

60 PRINT #3,CHR$(27);”P”;

70 PRINT #3,”PICA CHARACTER 2”\\\\

80 LIST #3

90 CLOSE #3

- ESC   M   			(1B, 4D) H   (27, 77) D

Input of this command designates the Elite Print mode.

Refer to 6.

- SI   				(0F) H   (15) D

Input of this command designates the Condensed Character mode.

OPEN #2, SER   ENTER

LIST   ENTER

10 OPEN #3,SER

20 REMark SMALL CHARACTER

30 PRINT #3,”PICA CHARACTER 1”\

40 PRINT #3,CHR$(15);

50 PRINT #3,”SMALL CHARACTER”\

60 PRINT #3,CHR$(28);

70 PRINT #3,”PICA CHARACTER 2”\\\\

80 CLOSE #3

CLOSE #2   ENTER

RUN   ENTER

- ESC   SI   			(1B, 0F)H   (27,15)D

This command is the same as the  SI  command.

Refer to 8.

- DC2  				(12)H   (18)D

Input of this command terminates the Condensed Character mode designated by the  SI   or  ESC   SI  command.

Refer to 8.

- ESC   x   (01) or (31)   		(1B, 78, 01) H   (27, 120, 1) D

(1B, 78, 31) H   (27, 120, 49) D

Input of this command designates the High Quality	Character mode and turns the NLQ lamp on. While in Condensed Character mode, if this command is performed, Standard characters	 are printed even though	the NLQ lamp is on. When the Con- densed	Character mode is terminated	 High Quality printing is performed.

10 OPEN #3, SER

20 REMark HIGH QUALITY (CORRESPONDENCE)

30 PRINT #3,”NORMAL QUALITY 1”\

40 PRINT #3,CHR$(27);”x1”;

50 PRINT #3,”HIGH QUALITY”\

60 PRINT #3,CHR$(27);’x0”;

70 PRINT #3,”NORMAL QUALITY 2”\\\\

80 LIST #3

90 CLOSE #3

- Esc   x   (00)  or   (30)  		(lB,  78,  00) H   (27, 120, 0) D,

(lB,  78,  30) H   (27, 120, 48) D

Input of this command terminates the High Quality Character mode and turns the NLQ lamp off. After this command is input the printer returns to Standard Character mode.

Refer to 11.

13.   ESC   p   (01) or (31)   		(lB, 70, 0l) H   (27, 112,  l) D,

(lB, 70, 31) H   (27, 112, 49) D

Input of this command designates the Proportional Character mode. In this mode the distance between characters varies.  When comparing Standard and High Quality Character	modes, notice must be taken of the character widths and spacings that differ.

10 OPEN #3,SER

20 REMark PROPORTIONAL

30 FOR I=32 TO 78

40 PRINT #3.CHRS(I);

50 NEXT I

60 PRINT #3,CHRS(27);"p1"\

70 FOR J=32 TO 78

80 PRINT #3,CHRS(J);

90 NEXT J

100 PRINT #3,CHRS(27);"p0"\

110 FOR K=32 TO 78

120 PRINT #3,CHRS(K);

130 NEXT K

140 PRINT #3,CHRS(13);\\\\

150 LIST #3

160 CLOSE #3

10 OPEN #3,SER

20 REMark PROPORTIONAL

30 FOR I=32 TO 78

40 PRINT #3.CHRS(I);

50 NEXT I

60 PRINT #3,CHRS(27);"p1"\

70 FOR J=32 TO 78

80 PRINT #3,CHRS(J);

90 NEXT J

100 PRINT #3,CHRS(27);"p0"\

110 FOR K=32 TO 78

120 PRINT #3,CHRS(K);

130 NEXT K

140 PRINT #3,CHR$(27);”x0”;

150 PRINT #3,CHRS(13);\\\\

160 LIST #3

170 CLOSE #3

14.    ESC   p   (00) or (30)  			(1B, 70, 00) H   (27, 112, 0) D

(1B, 70, 30) H   (27, 112, 48) D

Input of this command terminates the Proportional Character mode.

Refer to 13.

15.  ESC   S   (00) or (30)  		(lB, 53, 00) H  (27, 83, 0) D

(lB, 53, 30) H  (27, 83, 48) D

Input of this command designates the Superscript Character mode,

10 OPEN #3,SER

20 REMark SUPERSCRIPT

30 PRINT #3,”X”;

40 PRINT #3,CHR$(27);”SO”;

50 PRINT #3,CHR$(15);

60 PRINT #3,”2”;

70 PRINT #3,CHR$(27);”T”;

80 PRINT #3,CHR$(18);

90 PRINT #3,”+X=Y”\\\

100 LIST #3

110 CLOSE #3

- ESC   S   (01) or (31)   	(1B, 53, 01) H   (27, 83, 1) D

(1B, 53, 3l) H   (27, 83, 49) D

Input of this command designates the Subscript Character mode,

10 OPEN #3,SER

20 REMark SUBSCRIPT

30 PRINT #3,”H”;

40 PRINT #3,CHR$(27);”S1”;

50 PRINT #3,”2”;

60 PRINT #3,CHR$(27);”T”;

70 PRINT #3,”O”\\\\

80 LIST #3

90 CLOSE #3

- ESC   T   			(1B, 54) H   (27,84) D

Input of this command terminates the Superscript/Subscript Character mode. Superscript/Subscript Character mode condenses the height of a standard character to ½ its original value. The characters are the same in either Standard or High Quality Character mode. If Proportional Character mode is designated while in Superscript/Subscript Character mode, character widths and spacings become the same as in Standard Character mode. Thus I fboth Superscript/Subscript Character mode and Proportional Character mode are designated while in High Quality Character mode, character widths and spacings between characters are different from the case in which Superscript/Subscript Character mode is not designated.

10 OPEN #3,SER

20 REMarkN HIGH QUALITY&PROPORTIONAL&SUPER

30 PRINT #3,CHR$(27);”x1”;

40 PRINT #3,CHR$(27);”p1”;

50 PRINT #3,CHR$(27);”S0”;

60 PRINT #3,”ABCDEFGhijklmn”\

70 PRINT #3,CHR$(27);”T”;

80 PRINT #3,”ABCDEFGhijklmn”\

90 PRINT #3,CHR$(27);”x0”;

100 PRINT #3,CHR$(27);”p0”\\\\

110 LIST #3

120 CLOSE #3

- ESC   4   			(1B, 34) h   (27, 52) D,   (9B, 34) H   (155, 52) D

Input of this command designates the Italic Character mode. All data following this command is printed in Italic. This command is ignored during the printing of graphic data.

10 OPEN #3,SER

20 REMark ITALIC CHARACTER

30 PRINT #3,”PICA CHARACTER 1”\

40 PRINT #3,CHR$(27);”4”;

50 PRINT #3,”ITALIC CHARACTER”\

60 PRINT #3,CHR$(27);”5”;

70 PRINT #3,”PICA CHARACTER 2”\\\\

80 LIST #3

90 CLOSE #3

- ESC   5 				(lB,35) H   (27, 53) D

Input of this command terminates the Italic Character mode.

Refer  to  18.

- ESC   !   n  			(lB,  21,  n) H   (27, 33,  n) D

1 <= n <= 63

Input of this command designates mixed modes of the Elite, Condensed, Bold, Double Strike, and Double   Width Character mode by changing the value of  n.

Each bit of n designates the following modes.

| n = | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

D7:  Always  0 ..... MSB  (Most  Significant  Bit)

D6:  Always  0

D5:  Double Width Character mode

D4:  Double Strike Character mode

D3:  Bold Character mode

D2:  Condensed Character mode

D1:  Always 0

D0:  Elite Character mode   .....   LSB  (Least   Significant  Bit)

Refer to the "MODE COMBINATIONS"  table below.

10 OPEN #3,SER

20 REMark	MODE SELECTION

30 PRINT #3,”ABCDEFGhijklmn"\

40 PRINT #3,CHR$(27);”!";CHR$(60);

50 PRINT #3,”ABCDEFGhijklmn"\

60 PRINT#3,CHR$(27);”@"\\\\

70 LIST #3

80 CLOSE #3

PRINT MODE COMBINATIONS SPECIFIED BY THE ESC,  !, n  COMMAND

| n | DW | OS | BO | CO | EL | Printed Example |
| --- | --- | --- | --- | --- | --- | --- |
| 0 |  |  |  |  |  |  |
| 1 |  |  |  |  | O |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  | O |  |
| 4 |  |  |  | O |  |  |
| 5 |  |  |  |  | O |  |
| 6 |  |  |  | O |  |  |
| 7 |  |  |  |  | O |  |
| 8 |  |  | O |  |  |  |
| 9 |  |  | O |  | O |  |
| 10 |  |  | O |  |  |  |
| 11 |  |  | O |  | O |  |
| 12 |  |  | O |  |  |  |
| 13 |  |  | O |  | O |  |
| 14 |  |  | O |  |  |  |
| I5 |  |  | O |  | O |  |
| 16 |  | O |  |  |  |  |
| 17 |  | O |  |  | O |  |
| 18 |  | O |  |  |  |  |
| 19 |  | O |  |  | O |  |
| 20 |  | O |  | O |  |  |
| 21 |  | O |  |  | O |  |
| 22 |  | O |  | O |  |  |
| 23 |  | O |  |  | O |  |
| 24 |  | O | O |  |  |  |
| 25 |  | O | O |  | O |  |
| 26 |  | O | O |  |  |  |
| 27 |  | O | O |  | O |  |
| 28 |  | O | O |  |  |  |
| 29 |  | O | O |  | O |  |
| 30 |  | O | O |  |  |  |
| 31 |  | O | O |  | O |  |

| OW: | Double Width | OS: Double Strike | BO: Bold |
| --- | --- | --- | --- |
| co: | Condensed | EL: Elite |  |

PRINT MODE COMBINATIONS SPECIFIED BY THE ESC, !,  n COMMAND

| n | DW | DS | 80 | CO | EL | Printed Example |
| --- | --- | --- | --- | --- | --- | --- |
| 32 | 0 |  |  |  |  |  |
| 33 | 0 |  |  |  | 0 |  |
| 34 | 0 |  |  |  |  |  |
| 35 | 0 |  |  |  | 0 |  |
| 36 | 0 |  |  | 0 |  |  |
| 37 | 0 |  |  |  | 0 |  |
| 38 | 0 |  |  | 0 |  |  |
| 39 | 0 |  |  |  | 0 |  |
| 40 | 0 |  | 0 |  |  |  |
| 41 | 0 |  | 0 |  | 0 |  |
| 42 | 0 |  | 0 |  |  |  |
| 43 | 0 |  | 0 |  | 0 |  |
| 44 | 0 |  | 0 |  |  |  |
| 45 | 0 |  | 0 |  | 0 |  |
| 46 | 0 |  | 0 |  |  |  |
| 47 | 0 |  | 0 |  | 0 |  |
| 48 | 0 | 0 |  |  |  |  |
| 49 | 0 | 0 |  |  | 0 |  |
| 50 | 0 | 0 |  |  |  |  |
| 51 | 0 | 0 |  |  | 0 |  |
| 52 | 0 | 0 |  | 0 |  |  |
| 53 | 0 | 0 |  |  | 0 |  |
| 54 | 0 | 0 |  | 0 |  |  |
| 55 | 0 | 0 |  |  | 0 |  |
| 56 | 0 | 0 | 0 |  |  |  |
| 57 | 0 | 0 | 0 |  | 0 |  |
| 58 | 0 | 0 | 0 |  |  |  |
| 59 | 0 | 0 | 0 |  | 0 |  |
| 60 | 0 | 0 | 0 |  |  |  |
| 61 | 0 | 0 | 0 |  | 0 |  |
| 62 | 0 | 0 | 0 |  |  |  |
| 63 | 0 | 0 | 0 |  | 0 |  |

| OW: Double Width | OS: Double Strike | BO: Bold |
| --- | --- | --- |
| co: Condensed | EL: Elite |  |

(3) Bold Character Mode

- ESC   E 				(lB, 45) H	(27, 69) D

Input of this command designates Bold Character mode. In this mode the print head is moved in the right direction 1/120 inch to print the same character once again.

If this command is set while in Condensed Character mode, Bold Pica (10 cpi) characters are printed. If the Bold Character mode is first terminated by the  ESC   F  command the printer returns to Condensed Character mode (17 cpi).

10 OPEN #3,SER

20 REMark BOLD CHARACTER

30 PRINT #3,”NORMAL CHARACTER”\

40 PRINT #3,CHR$(15);

50 PRINT #3,”SMALL CHARACTER”\

60 PRINT #3,CHR$(27);”E”;

70 PRINT #3,”BOLD CHARACTER”\

80 PRINT #3,CHR$(27);”F”;

90 PRINT #3,”SMALL CHARACTER 2”\

100 PRINT #3,CHR$(18)\\\\

110 LIST #3

120 CLOSE #3

- ESC   F 			(1B, 46) H	(27,70) D

Input of this command terminates the Bold Character mode.

Refer to 21.

- Double Strike Character Mode

- ESC   G 				(1B, 47) H	(37, 71) D

Input of this command designates the Double Strike Character mode. In this mode the paper moves up 1/144 inch and prints the same character once again.

The Double Strike function is only able to be performed on Standard characters. If the Double Strike Character mode is set and is overlapped with Superscript/Subscript or High Quality character mode, Superscript/Subscript or High Quality Character mode is given priority. The printer returns to Double Strike Character mode once the other modes are terminated.

10 OPEN #3,SER

20 REMark DOUBLE STRIKE

30 PRINT #3,”NORMAL CHARACTER”\

40 PRINT #3,CHR$(27);”G”;

50 PRINT #3,”DOUBLE STRIKE CHARACTER”\

60 PRINT #3,CHR$(27);”x1”;

70 PRINT #3,”NO DOUBLE HIGH QUALITY”\

80 PRINT #3,CHR$(27);”x0”;

90 PRINT #3,”DOUBLE STRIKE CHARACTER 2”\

100 PRINT #3,CHR$(27);”H”\\\\

110 LIST #3

120 CLOSE #3

- ESC   H  				(1B, 48) H	(27, 72) D

Input of this command terminates the Double Strike Character mode.

Refer to 23.

- Double Width Character Mode

- SO  				(0E) H		(14) D

Input of this command designates Double Width Character mode. This command is not valid for graphic data. If more than a single line of character data is input, printing and a line feed are auotmatically performed and this command is terminated. This command is also terminated by  DC4 ,  ESC   W   n  or line feed commands other than the  ESC   J   n  command.

10 OPEN #3,SER

20 REMark DOUBLE WIDTH

30 PRINT #3,”NORMAL SIZE CHARACTER 1”\

40 PRINT #3,CHR$(14);

50 PRINT #3,”DOUBLE WIDTH”\

60 PRINT #3,CHR$(20);

70 PRINT #3,”NORMAL SIZE CHARACTER 2”\\\\

80 LIST #3

90 CLOSE #3

- ESC   SO  			(1B, 0E) H   (27,14) D

Same as the   SO   command.

Refer to 25.

- DC4  				(14) H   (20) D

Input of this command terminates the Double Width Character mode designated by the   SO  command.

Refer to 25.

- ESC   WI   (0l) or (31)  		(lB, 57, 0l) H    (27, 87, 1) D,

(IB, 57, 3l) H	  (27, 87, 49) D

Input of this command designates Double Width Character	mode that will not be terminated by a line  feed.  This command terminates a   SO  Double Width Character mode command.

10 OPEN #3,SER

20 REMark DOUBLE WIDTH NOT CLEARED BY LF

30 PRINT #3,CHR$(14);

40 PRINT #3,”DOUBLE WIDTH 1”\

50 PRINT #3,”DOUBLE WIDTH 2”\

60 PRINT #3,CHR$(27);”W1”;

70 PRINT #3,”DOUBLE WIDTH 3”\

80 PRINT #3,”DOUBLE WIDTH 4”\

90 PRINT #3,CHR$(27);”W0”;

100 PRINT #3,”STANDARD WIDTH”\\\\

110 LIST #3

120 CLOSE #3

29.  ESC   W   (00) or (30)  	  	(lB, 57, 00) H   (27, 87, 0) D,

(lB, 57, 30) H   (27, 87, 48) D

Input of this command terminates the Double Width Character mode of  ESC   W   (01)  that is not terminated by a line feed command. The Double Width Character mode designatedby the  SO  command is also terminated.

Refer to  28.

- Graphic Print Mode

- ESC   K   n1   n2  		(1B, 4B, n1, n2) H	(27, 75, n1, n2) D

Input of this command designates Standard Density Graphics printing. The maximum number of horizontal dots is 480. n1 and n2 are binary numbers that specify the graphic data number. The graphic data number is calculated as n1 + 256 x n2. n2 is the high order bit and n1 is the low order bit. After this command the printer returns to the prior print state. If n1 and n2 specify a number that exceeds a single line worth of dots, automatic printing is performed without a line feed and the exceeding dots are cleared.

Graphic Data and the Corresponding Dots

Inputting the ESC A (08) command is useful in graphics mode since the patterns then appear continuous.

10 OPEN #3,SER

20 REMark STANDARD GRAPHIC

30 PRINT #3,CHR$(27);”A”;CHR$(8);

40 FOR I = 1 TO 3

50 PRINT #3,CHR$(27);”K”;CHR$(0);CHR$(1);

60 FOR J = 0 TO 255

70 PRINT #3,CHR$(J);

80 NEXT J

90 PRINT #3,CHR$(10);

100 NEXT I

110 PRINT #3,CHR$(27);”2”\\\\

120 LIST #3

130 CLOSE #3

- ESC   L   n1   n2 				(lB, 4C, n1, n2) H   (27, 76, n1, n2) D

Input of this command designates Double Density Graphic printing.  The maximum number of horizontal dots is 960.  The print speed is half as fast as Standard Density Graphic printing.  n1 and n2 are binary numbers that indicate the number of graphic data that follow.  n1 is the low byte and n2 is the high byte.  The others are the same as the  ESC   K  code.

10 OPEN #3,SER

20 REMark DOUBLE DENSITY

30 PRINT #3,CHR$(27);”A”;CHR$(8);

40 FOR I = 1 TO 3

50 PRINT #3,CHRS(27);"L";CHRS(0);CHR$(1);

60 FOR J = O TO 255

70 PRINT #3,CHRS(J);

80 NEXT J

90 PRINT #3,CHR$(10);

100 NEXT I

110 PRINT #3,CHR$(27);"2"\\\\

120 LIST #3

130 CLOSE #3

- ESC   Y   n1   n2   		(1B, 59, n1 n2) H   (27, 89, n1, n2) D

Input of this command designates Double Speed Double-Density Graphic printing. The maximum number of horizontal dots is 960. Horizontally aligned dots are not printed. Therefore, the number of dots that can be printed continuously in a horizontal direction is 480. The print speed is the same as Standard Density Graphic mode. The rest is the same as the   ESC   K   command.

Example 1.  Input data: (1B, 59, 03, 00, FF, FF) H

The second dot column cannot be printed.

Example 2.  Input data (1B, 59, 03, 00, AA, 55, AA) H

All the dots specified in this case can be printed.

10 OPEN #3,SER

20 REMark DOUBLE DENSITY & SPEED

30 PRINT #3,CHR$(27);”A”;CHR$(8);

40 FOR I = 1 TO 3

50 PRINT #3,CHR$(27);”Y”;CHR$(0);CHR$(1);

60 FOR J = 0 TO 255

70 PRINT #3,CHR$(J);

80 NEXT J

90 PRINT #3,CHR$(10);

100 NEXT I

110 PRINT #3,CHR$(27);”2”\\\\

120 LIST #3

130 CLOSE #3

- ESC   Z   n1   n2   		(1B, 5A, n1 n2) H   (27, 90, n1, n2) D

Input of this command designates Quadruple Density Graphic printing. The maximum number of horizontal dots is 1920. Horizontally aligned dots are not printed. Therefore, the number of dots that can be printed continuously in a horizontal direction is 960. The print speed is the same as Double Density Graphic speed. The rest is the same as the   ESC   K   command.

10 OPEN #3,SER

20 REMark 4 TIMES DENSITY

30 PRINT #3,CHR$(27);”A”;CHR$(8);

40 FOR I = 1 TO 3

50 PRINT #3,CHR$(27);”Z”;CHR$(0);CHR$(1);

60 FOR J = 0 TO 255

70 PRINT #3,CHR$(J);

80 NEXT J

90 PRINT #3,CHR$(10);

100 NEXT I

110 PRINT #3,CHR$(27);”2”\\\\

120 LIST #3

130 CLOSE #3

- ESC   *   m   n1   n2  			(lB, 2A, m, nl, n2) H   (27, 42, m, n1, n2) D

0 <= m <= 6

Input of this command allows Graphic types to be printed.  As shown below in the table, m determines the following print types.  As in the   ESC   K  command, nl and n2 is the Graphic Data number.

| m | Graphic Type | 1 Line Dot Number (8inch) | Horizontal Dot Spacing | Vertical: Horizontal | Equivalent Commands |
| --- | --- | --- | --- | --- | --- |
| 0 | Single Density Graphic | 480 dot | 1/60 inch | 1:1.2 | ESK, K |
| 1 | Double Density Graphic | 960 dot | 1/120 inch | 1:0.6 | ESC, L |
| 2 | Double-Speed Double-Density Graphic | 960 dot | 1/120 inch | 1:0.6 | ESC,Y |
| 3 | Quadruple Density Graphic | 1920 dot | 1/240 inch | 1:0.3 | ESC, Z |
| 4 | 640 Dot Graphic | 640 dot | 1/80 inch | 1:0.9 | - |
| 5 | 576 Dot Graphic | 576 dot | 1/72 inch | 1:1 | - |
| 6 | 720 Dot Graphic | 720 dot | 1/90 inch | 1:0.8 | - |

10 OPEN #3,SER

20 REMark GRAPHIC SELECTION

30 PRINT #3,CHR$(27);"A";CHR$(8);

40 FOR I=1 TO 3

50 PRINT #3,CHR$ (27);"*";CHR$(5);CHR$(0);CHR$(1);

60 FOR J=0 TO 255

70 PRINT #3,CHRS(J);

80 NEXT J

90 PRINT #3,CHRS(10);

100 NEXT I

110 PRINT #3,CHRS(27);"2"\\\\

120 LIST #3

130 CLOSE #3

- ESC   ^   a   n1   n2   HB   LB   	(1B, 5E, a, n1, n2) H   (27,94,a,n1,n2) D

Input of this command designates 9-pin graphic mode.

The maximum number of horizontal dots is 480 when a = 0 and it is 960 when a = 1. Since 1 dot column is composed of 9 vertical dots, 2 bytes are used to designate a data. The rest is the same as the   ESC   K   command.

Example:

10 OPEN #3,SER

20 REMark 9 PIN GRAPHIC

30 PRINT #3,”9 PIN GRAPHIC”;CHR$(13);

40 PRINT #3,CHR$(27);”^”;CHR$(0);CHR$(80);CHR$(1);

50 FOR I = 1 TO 80

60 PRINT #3,CHR$(0);CHR$(128);

70 NEXT I

80 FOR I=0 TO 255

90 PRINT #3,CHR$(I);CHR$(128);

100 NEXT I

110 PRINT #3,CHR$(27);”@”;\\\\

120 LIST #3

130 CLOSE #30

- Line Feed Spacing

- ESC   0   			(1B, 30) H   (27, 48) D

Input of this command designates a line feed value of 1/8 inch.

10 OPEN #3,SER

20 REMark 1/8 INCHES LINE SPACING

30 PRINT #3,CHR$(27);”0”;

40 FOR I=1 TO 6

50 PRINT #3,”LINE FEED”;I;

60 PRINT #3,CHR$(10);

70 NEXT I

80 PRINT #3,”END”

90 PRINT #3,CHR$(27);”2”\\\\

100 LIST #3

110 CLOSE #3

- ESC   1   			(1B, 31) H   (27, 49) D

Input of this command designates a line feed value of 7/72 inches.

10 OPEN #3,SER

20 REMark 7/72 INCHES LINE SPACING

30 PRINT #3,CHR$(27);”1”;

40 FOR I=1 TO 6

50 PRINT #3,”LINE FEED”;I;

60 PRINT #3,CHR$(10);

70 NEXT I

80 PRINT #3,”END”

90 PRINT #3,CHR$(27);”2”\\\\

100 LIST #3

110 CLOSE #3

- ESC   2  				(1B, 32) H   (27, 50) D

The linefeed value is designated as 1/6 inch.

10 OPEN #3,SER

20 REMark 1/6 INCHES LINE SPACING

30 PRINT #3,CHR$(27);”2”;

40 FOR I=1 TO 6

50 PRINT #3,”LINE FEED”;I;

60 PRINT #3,CHR$(10);

70 NEXT I

80 PRINT #3,”END”

90 PRINT #3,CHR$(27);”2”\\\\

100 LIST #3

110 CLOSE #3

- ESC   3   n   			(1B, 33, n) H   (27, 51, n) D

0 <= n <= 255

Input of this command designates a line feed value of n/216 inch.

10 OPEN #3,SER

20 REMark n/216 INCHES LINE SPACING

30 FOR I=20 to 60 STEP 5

40 PRINT #3,CHR$(27);”3”;CHR$(I);

50 PRINT #3,”LINE FEED”;I;”/216”;

60 PRINT #3,CHR$(10);

70 NEXT I

80 PRINT #3,”END”

90 PRINT #3,CHR$(27);”2”\\\\

100 LIST #3

110 CLOSE #3

- ESC   A   n   			(1B, 41, n) H   (27, 65, n) D,

0 <= n <=85    Ignored if n >= 86

Input of this command desigantes a line feed value of n/72 inch.

10 OPEN #3,SER

20 REMark n/72 INCHES LINE SPACING

30 PRINT #3,CHR$(27);”A”;CHR$(18);

40 FOR I=1 TO 6

50 PRINT #3,”LINE FEED”;I;

60 PRINT #3,CHR$(10);

70 NEXT I

80 PRINT #3,”END”

90 PRINT #3,CHR$(27);”2”\\\\

100 LIST #3

110 CLOSE #3

- Page Length Setting

- ESC   C   n   			(1B, 43, n) H   (27, 67, n) D,

1 <= n <= 127

Input of this command designates the page length in line units, n specifies the number of lines per page. The length of the page is determined by multiplying the line feed value to n.

The position of the paper, at the time this command is performed, is taken as the top of the form.

The page length is not altered even if the line feed value is changed.

If n >= 128 the three bytes of this command are ignored.

10 OPEN #3,SER

20 REMark PAGE LENGTH

30 PRINT #3,CHR$(27);”C”;CHR$(5);

40 PRINT #3”START”\

50 PRINT #3,”PAGE 1”\

60 PRINT #3,CHR$(12);

70 PRINT #3,”PAGE 2”\

80 PRINT #3,CHR$(12);

90 PRINT #3,”PAGE 3”\

100 PRINT #3,”END”

110 PRINT #3,CHR$(27);”C”;CHR$(66)\\\\

120 LIST #3

130 CLOSE #3

- ESC   C   (00)   n   		(1B, 43, 00, n) H   (27, 67, 0, n) D

1 <= n <= 22

Input of this command designates the page length in inch units, n refers to the inch unit.

If n>= 23 or n = 0, the 3 bytes of this command are ignored.

10 OPEN #3,SER

20 REMark PAGE LENGTH

30 PRINT #3,CHR$(27);”C”;CHR$(0);CHR$(1);

40 PRINT #3”START”\

50 PRINT #3,”PAGE 1”\

60 PRINT #3,CHR$(12);

70 PRINT #3,”PAGE 2”\

80 PRINT #3,CHR$(12);

90 PRINT #3,”PAGE 3”\

100 PRINT #3,”END”

110 PRINT #3,CHR$(27);”C”;CHR$(0);CHR$(11)\\\\

120 LIST #3

130 CLOSE #3

- Horizontal Tab Setting

- ESC   D   n1   n2   …   nk   NUL

(1B, 44, n1, n2, …, nk, 00) H   (27, 68, n1, n2, …, nk, 0) D

1 <= k <= 28	     IF k >= 29, nk is ignored.

Input of this command designates the Horizontal Tab. The maximum number of Horizontal Tab settings is 28.

At power-on the Horizontal Tab is set at every eight character location. This command alters these settings.

n is a binary number that is multiplied to the present character width to set the Horizontal Tab location. The Horizontal Tab settings are to be done in order from the smallest to largest value. The setting process is terminated by the  NUL  code.

10 OPEN #3,SER

20 REMark HORIZONTAL TAB SETTING

30 PRINT #3,”01234567890123456789012345”\

40 PRINT #3,CHR$(27);”D”;CHR$(4);CHR$(12);CHR$(0);

50 FOR I = 1 TO 2

60 PRINT #3,CHR$(9);

70 PRINT #3,”TAB”;I;

80 NEXT I

90 PRINT #3,CHR$(10);

100 PRINT #3,CHR$(27);”@”;\\\\

110 LIST #3

120 CLOSE #3

- HT  				(09) H   (9) D

Data input following this command is printed from the next Horizontal Tab location.

10 OPEN #3,SER

20 REMark DEFAULT TAB

30 PRINT #3,”0123456789012345678901234”\

40 FOR I=1 TO 3

50 PRINT #3,CHR$(9);

60 PRINT #3,”TAB”;I;

80 NEXT I

90 PRINT #3,CHR$(10);

100 PRINT #3,CHR$(27);”@”;\\\\

110 LIST #3

      - OSE #3

- Margin Setting

- ESC   Q   n  			(1B, 51, n) H   (27, 81, n) D

Input of this command designates the right margin. n specifies the column number according to the present character width. If the value of n exceeds the column number of a single line the three bytes of this command are ignored.

This command is also ignored when the distance between the left and right margins is less than the character width of a single Pica Double Width character.

Input of this command clears all print data input prior to this command.

10 OPEN #3,SER

20 REMark RIGHT MARGIN

30 PRINT #3,”0123456789012345678901234”\

40 PRINT #3,CHR$(27);”Q”;CHR$(20);

50 FOR I = 1 TO 6

60 PRINT #3,”MARGIN”;

70 NEXT I

80 PRINT #3,CHR$(10);

90 PRINT #3,CHR$(27);”@”;\\\\

100 LIST #3

110 CLOSE #3

- ESC   l   n   			(1B, 6C, n) H   (27, 108, n) D

(N.B.  1  is lower case letter L)

Input of this command designates the left margin. n specifies the column number according to the present character width. If the value of n exceeds the column number of a single line the three bytes of this command are ignored.

If the left margin setting exceeds the right margin setting this command is ignored. This command is also ignored when the distance between the left and right margins is less than the character width of a single Pica Double Width character.

10 OPEN #3,SER

20 REMark LEFT MARGIN

30 PRINT #3,”0123456789012345678901234”\

40 PRINT #3,CHR$(27);”l”;CHR$(10);

50 PRINT #3,”LEFT MARGIN START LINE”\

60 PRINT #3,”LEFT MARGIN NO.2 LINE”\

70 PRINT #3,”LEFT MARGIN END LINE”\

80 PRINT #3,CHR$(27);”l”;CHR$(0);

90 PRINT #3,”START POSITION 0”\

100 PRINT #3,CHR$(27);”@”;\\\\

110 LIST #3

120 CLOSE #3

- Underline

- ESC   -   (01) or (31)   			(1B, 2D, 01) H   (27, 45, 1) D

(1B, 2D, 31) H   (27, 45, 49) D

Input of this command underlines each character input following the command. This excludes graphic data of all categories.

An underline is added to space code. If the printing location is shifted due to the  HT  command the blanked are is not underlined.

10 OPEN #3,SER

20 REMark UNDERLINE

30 PRINT #3,”PERSONAL “;

40 PRINT #3,CHR$(27);”-“;CHR$(1);

50 PRINT #3,”COMPUTER”\

60 PRINT #3,”COLOR”;

70 PRINT #3,CHR$(9);

80 PRINT #3,”TELEVISION”\

90 PRINT #3,”VIDEO  TAPE”\

100 PRINT #3,CHR$(27);”-“;CHR$(0);

110 PRINT #3,”ELECTRONICS”\\\\

120 LIST #3

130 CLOSE #3

- ESC   -   (00) or (30)   			(1B, 2D, 00) H   (27, 45, 0) D,

(1B, 2D, 30) H   (27, 45, 48) D

Input of this command terminates the Underline command.

Refer to 47.

- Buffer Clear

- CAN  				(18) H   (24) D

Input of this command clears all previously input print data. Control Functions, however, are still valid. (The printer mode is not altered)

10 OPEN #3,SER

20 REMark BUFFER CLEAR

30 PRINT #3,CHR$(27);”x1”;

40 PRINT #3,”ABCDEFGHIJKLMN”\

50 PRINT #3,”ABCDEFG”;

60 PRINT #3,CHR$(24);

70 PRINT #3,”HIJKLMN”\

80 PRINT #3;CHR$(27);”x0”;\\\

90 LIST #3

100 CLOSE #3

- Back Space

- BS  				(08) H   (8) D

If this command is input, after printing of the present data, the print initiation position is moved to the left by a single character width.

10 OPEN #3,SER

20 REMark BACK SPACE

30 PRINT #3,”---------”;

40 PRINT #3,CHR$(8);CHR$(8);CHR$(8);

50 PRINT #3,”|||||||||”\

60 PRINT #3,CHR$(27);”@”;\\\\\

70 LIST #3

80 CLOSE #3

- Buzzer

- BEL  			(07) H   (7) D

Input of this command causes the buzzer to sound for approximately 0.3  seconds.

- Home Positioning

- ESC   <   			(1B, 3C) H   (27, 60) D

Input of this command moves the print head to the home position.

- Skip-over  Perforation

- ESC   N   n   			(lB, 4E, n) H   (27,78,	n) D,

1 <= n <= 127

Input of this command designates skip perforation. n specifies the number of lines to be skipped over. If the remainder of the page is less than the value in n, the printer automatically performs a form feed making the top of the next page the printing position.

If n = 0 or n >= 128 this command is ignored.

If the skip value exceeds 1 page this command is ignored.

10 OPEN #3,SER

20 REMark	SKIP	PERFORATION

30 PRINT #3,CHRS(27);"C";CHRS(5);

40 PRINT #3,CHRS(27);"N";CHRS(2);

50 FOR I=1 TO 5

60 PRINT #3,"SKIP LINE";I\

70 NEXT I

80 PRINT #3,CHR$(12);

90 PRINT #3,CHRS(27);"O";

100 FOR 1=1 TO 5

110 PRINT #3,"NORMAL LINE”;I\

120 NEXT I

130 PRINT #3,CHR$(10);

140 PRINT #3,CHR$(27);”@”;\\\\

150 LIST #3

160 CLOSE	#3

- ESC   O   			(1B, 4F) H   (27, 79) D

Input of this command terminates the skip-over perforation command.

Refer to 53.

- Paper Out Detection

- ESC   8   				(1B, 38) H   (27, 56) D

Input of this command makes the printer ignore the paper out detection function.

- ESC   9   				(1B, 40) H   (27, 57) D

Input of this command makes the paper out detection function valid.

- Reset

- ESC   @   			(1B, 40) H   (27, 64) D

Input of this command puts the printer into the same state as the power-on state. All data input prior to this command is ignored. The first data following this command is not guaranteed.

10 OPEN #3,SER

20 REMark RESET

30 PRINT #3,CHR$(27);”4”;

40 PRINT #3,”ITALIC CHARACTER 1”;

50 PRINT #3,CHR$(27);”@”;

60 PRINT #3,”ITALIC CHARACTER 2”\\\

70 LIST #3

80 CLOSE #3

- Unidirectional Printing

- ESC   U   (01) or (31)   			(1B, 55, 01) H   (27, 85, 1) D,

(1B, 55, 31) H   (27, 85, 49) D

All data that is input after this command is printed from left to right.

10 OPEN #3,SER

20 REMark UNIDIRECTIONAL

30 PRINT #3,CHR$(27);”1”;

40 PRINT #3,CHR$(27);”U1”;

50 PRINT #3,”------------------------“;CHR$(13);

60 PRINT #3,”||||||||||||||||||||||||”\

70 PRINT #3,”||||||||||||||||||||||||”\

80 PRINT #3,”||||||||||||||||||||||||”\

90 PRINT #3,”||||||||||||||||||||||||”;CHR$(13);

100 PRINT #3,”------------------------“\

110 PRINT #3,CHR$(27);”U0”;

120 PRINT #3,”    -------  -------    “;CHR$(13);

130 PRINT #3,”    |||||||  |||||||    “\

140 PRINT #3,”    |||||||  |||||||    “\

150 PRINT #3,”    |||||||  |||||||    “\

160 PRINT #3,”    |||||||  |||||||    “;CHR$(13);

170 PRINT #3,”    -------  -------    “\

180 PRINT #3,CHR$(27);”2”\\\\

190 LIST #3

200 CLOSE #3

- ESC   U   (00) or (30)   			(1B, 55, 00) H   (27, 85, 0) D,

(1B, 55, 30) H   (27, 85, 48) D

Input of this command terminates the above  ESC   U   (01)  command.

Refer to 58.

_DIP SWITCH SETTING____________________________________

The following function can be selected by using the DIP switches located at the back of the printer. The DIP switches are read after the initialisation process. This is done by either turning the power switch on or by input of an  ESC   @  command.

| Switch No. | Function | ON | OFF | Setting as shipped |
| --- | --- | --- | --- | --- |
| 1-1 | Baud rate selection | See below | OFF |
| 1-2 |  |  | OFF |
| 1-3 | Page length setting | 12 inches | 11 inches | OFF |
| 1-4 | Character zero shape selection | 0 | 0 | OFF |

| Switch 1-1 | Switch 1-2 | Baud rate |
| --- | --- | --- |
| OFF | OFF | 9600 |
| ON | OFF | 4800 |
| OFF | ON | 2400 |
| ON | ON | 1200 |

_SERIAL INTERFACE_____________________________________

RS-232C, 25-pin D male.

Pin configuration of the input connector.

| PIN | SIGNAL | EXPLANATION |
| --- | --- | --- |
| 1 | FG | Frame Ground |
| 3 | RXD | Input data |
| 7 | SG | Signal Ground |
| 20 | DTR | BUSY/READY state fo the printer ON (+3 ~ +25V) … Ready to receive data OFF (-3 ~ -25V) … Busy |

_CHARACTER SET TABLE_________________________________

_TROUBLESHOOTING____________________________________

Use the table below to diagnose any problems that may occur. If you cannot solve the problem, try to decide what part of your system is not working properly and consult your dealer.

| PROBLEM | CAUSE AND REMEDY |
| --- | --- |
| The printer does not print. The POWER lamp does not light. | 1) Power is not getting to the printer. Check the power cord and power switch. |
| The printer does not print. The POWER lamp is lit. | 1) The connection to the computer is not correct. Check to make sure that the cable connecting the printer and computer is correctly connected. 2) The ribbon cassette is not properly installed. Properly install it. |
| The printer is operating properly, but the paper is not feeding through properly. | 1) The paper is jammed in the printer. Remove the paper and reinsert it properly. |
| The print is light or smeared. | 1) The printhead position is not correct. Move the head adjustment lever to match the paper being used. 2) The ribbon cassette is not properly installed. Properly install the cassette. 3) The ink ribbon is old or is worn out. Replace the old ribbon cassette with a new one. |
| The P.OUT lamp is blinking. | 1) An error condition has been detected. Turn power off and then back on again. |

_CAUTIONS FOR USE_____________________________________

- Do not use a power supply voltage which is out of the specified range.

- Do not touch the print head immediately after printing because it is too hot.

- Be careful not to twist the ribbon while installing it.

- Wait at least two seconds after turning power off before turning it back on again. The initialization process may not be performed correctly if this is not done.

- The printer should be used where the humidity is low, there is little dust, and where it is not in direct sunlight.

- Do not perform printing without the ribbon cassette and paper properly installed.

- Never install the tractor unit when using friction feed for cut sheet paper.

- When using continuous forms, the paper bail must be set to the platen side otherwise a paper jam may occur.

Sinclair reserves the right to change the contents as stated herein at any time and without notice. Although every effort has been made to insure that the contents as stated herein are complete and without error, Sinclair cannot be responsible for any damage that may occur should this not be the case.

# _APPENDIX A (Specifications)______________________________

- SPECIFICATIONS

- Dimensions		W390 x H119 x D266mm

- Weight			Approximately 4.9 kg

- Temperature		5 ~ 35°C, during operation

- Humidity		20-80%, during operation (No condensation)

- Power Supply		117 VAC ± 10%, 220/240 VAC ± 10% 50/60 Hz ± 3%

- Power Consumption	30 watts (Self test printing)

15 watts (Stand-by)

- PRINTING SPECIFICATIONS

- Print Method		Impact Dot Matrix (Bi-directional Logic Seeking)

- Print Head		9-pin

- Character Category	160 characters

- Graphic Printing	7 categories

480#, 576, 640, 720, 960#, 960*, 1920* (dot columns/line)

* dots that are horizontally aligned cannot be printed.

# 9 vertical dots printing is possible.

- Print Mode		Standard Pica			10 CPI

Standard Elite			12 CPI

Standard Condensed		17 CPI

High Quality Pica		10 CPI

High Quality Elite		12 CPI

7 Categories of Graphic Printing

Mixing any of the above modes within a single line is possible.

In addition, this printer is capable of Bold, Double Strike, Double Width, Superscript/Subscript, Proportional, and Italic character modes.

- Paper Feed Method	Friction method

Tractor method

- Line Feed Pitch		Minimum of 1/216 inch

- Line Feed Speed		6.7 lines/second (6 lines/inch)

10 lines/second (9 lines/inch)

(during continuous linefeed by the LF and FF switch)

- Printing Forms		Paper width		4 inches – 10 inches

Paper thickness	15lbs – 20lbs in U.S.A.

(52 g/m² - 76 g/m²)

0.07 mm – 0.1 mm

- Multiple Copies		Original plus 2, non-carbon paper

Total thickness of less than 0.2 mm

- Ribbon			Cassette style, single color (Black)

_APPENDIX B (Character Category Priority Table)_____________

CHARACTER CATEGORY PRIORITY TABLE

* In print mode the following priorities exist.

1. Elite > Proportional > Bold > Condensed > Pica

2. Superscript/Subscript	> High Quality > Double Strike

Examples:

- If the Elite, Condensed, Superscript, and Double Strike modes are designated, according to Priority chart No. 84, Elite Superscript characters will be printed.

- If the Elite mode is terminated from the above example, Condensed Superscript characters will be printed according to No. 20.

- If the Superscript mode is terminated from example a., Elite Double Strike characters will be printed according to No. 83.

Prop: Proportional     Cond: Condensed     H.Q.: High Quality     D.S.: Double Strike     Sup/Sub: Superscript/Subscript

|  | Command Combination | Character Mode Printed | Printed Ex. |
| --- | --- | --- | --- |
| No. | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | Pica | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | ABChijk |
| 1 |  |  |  |  |  |  |  | O |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  | O | O |  |  |  |  |  |  | O |  |
| 3 |  |  |  |  |  | O |  | O |  |  |  |  |  | O |  |  |
| 4 |  |  |  |  |  | O | O | O |  |  |  |  |  |  | O |  |
| 5 |  |  |  |  | O |  |  | O |  |  |  |  | O |  |  |  |
| 6 |  |  |  |  | O |  | O | O |  |  |  |  |  |  | O |  |
| 7 |  |  |  |  | O | O |  | O |  |  |  |  | O |  |  |  |
| 8 |  |  |  |  | O | O | O | O |  |  |  |  |  |  | O |  |
| 9 |  |  |  | O |  |  |  | O |  |  |  | O |  |  |  |  |
| 10 |  |  |  | O |  |  | O | O |  |  |  | O |  |  | O |  |
| 11 |  |  |  | O |  | O |  | O |  |  |  | O |  | O |  |  |
| 12 |  |  |  | O |  | O | O | O |  |  |  | O |  |  | O |  |
| 13 |  |  |  | O | O |  |  | O |  |  |  | O | O |  |  |  |
| 14 |  |  |  | O | O |  | O | O |  |  |  | O |  |  | O |  |
| 15 |  |  |  | O | O | O |  | O |  |  |  | O | O |  |  |  |
| 16 |  |  |  | O | O | O | O | O |  |  |  | O |  |  | O |  |
| 17 |  |  | O |  |  |  |  |  |  |  | O |  |  |  |  |  |
| 18 |  |  | O |  |  |  | O |  |  |  | O |  |  |  | O |  |
| 19 |  |  | O |  |  | O |  |  |  |  | O |  |  | O |  |  |
| 20 |  |  | O |  |  | O | O |  |  |  | O |  |  |  | O |  |
| 21 |  |  | O |  | O |  |  |  |  |  | O |  |  |  |  |  |
| 22 |  |  | O |  | O |  | O |  |  |  | O |  |  |  | O |  |
| 23 |  |  | O |  | O | O |  |  |  |  | O |  |  | O |  |  |
| 24 |  |  | O |  | O | O | O |  |  |  | O |  |  |  | O |  |
| 25 |  |  | O | O |  |  |  | O |  |  |  | O |  |  |  |  |
| 26 |  |  | O | O |  |  | O | O |  |  |  | O |  |  | O |  |
| 27 |  |  | O | O |  | O |  | O |  |  |  | O |  | O |  |  |
| 28 |  |  | O | O |  | O | O | O |  |  |  | O |  |  | O |  |
| 29 |  |  | O | O | O |  |  | O |  |  |  | O |  |  |  |  |
| 30 |  |  | O | O | O |  | O | O |  |  |  | O |  |  | O |  |
| 31 |  |  | O | O | O | O |  | O |  |  |  | O |  | O |  |  |
| 32 |  |  | O | O | O | O | O | O |  |  |  | O |  |  | O |  |
| 33 |  | O |  |  |  |  |  | O |  | O |  |  |  |  |  |  |
| 34 |  | O |  |  |  |  | O | O |  | O |  |  |  |  | O |  |

Prop: Proportional     Cond: Condensed     H.Q.: High Quality     D.S.: Double Strike     Sup/Sub: Superscript/Subscript

|  | Command Combination | Character Mode Printed | Printed Ex. |
| --- | --- | --- | --- |
| No. | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | Pica | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | ABChijk |
| 35 |  | O |  |  |  | O |  |  |  | O |  |  |  | O |  |  |
| 36 |  | O |  |  |  | O | O |  |  | O |  |  |  |  | O |  |
| 37 |  | O |  |  | O |  |  |  |  | O |  |  | O |  |  |  |
| 38 |  | O |  |  | O |  | O |  |  | O |  |  |  |  | O |  |
| 39 |  | O |  |  | O | O |  |  |  | O |  |  | O |  |  |  |
| 40 |  | O |  |  | O | O | O |  |  | O |  |  |  |  | O |  |
| 41 |  | O |  | O |  |  |  |  |  | O |  | O |  |  |  |  |
| 42 |  | O |  | O |  |  | O |  |  | O |  | O |  |  | O |  |
| 43 |  | O |  | O |  | O |  |  |  | O |  | O |  | O |  |  |
| 44 |  | O |  | O |  | O | O |  |  | O |  | O |  |  | O |  |
| 45 |  | O |  | O | O |  |  |  |  | O |  | O | O |  |  |  |
| 46 |  | O |  | O | O |  | O |  |  | O |  | O |  |  | O |  |
| 47 |  | O |  | O | O | O |  |  |  | O |  | O | O |  |  |  |
| 48 |  | O |  | O | O | O | O |  |  | O |  | O |  |  | O |  |
| 49 |  | O | O |  |  |  |  |  |  | O |  |  |  |  |  |  |
| 50 |  | O | O |  |  |  | O |  |  | O |  |  |  |  | O |  |
| 51 |  | O | O |  |  | O |  |  |  | O |  |  |  | O |  |  |
| 52 |  | O | O |  |  | O | O |  |  | O |  |  |  |  | O |  |
| 53 |  | O | O |  | O |  |  |  |  | O |  |  | O |  |  |  |
| 54 |  | O | O |  | O |  | O |  |  | O |  |  |  |  | O |  |
| 55 |  | O | O |  | O | O |  |  |  | O |  |  | O |  |  |  |
| 56 |  | O | O |  | O | O | O |  |  | O |  |  |  |  | O |  |
| 57 |  | O | O | O |  |  |  |  |  | O |  | O |  |  |  |  |
| 58 |  | O | O | O |  |  | O |  |  | O |  | O |  |  | O |  |
| 59 |  | O | O | O |  | O |  |  |  | O |  | O |  | O |  |  |
| 60 |  | O | O | O |  | O | O |  |  | O |  | O |  |  | O |  |
| 61 |  | O | O | O | O |  |  |  |  | O |  | O | O |  |  |  |
| 62 |  | O | O | O | O |  | O |  |  | O |  | O |  |  | O |  |
| 63 |  | O | O | O | O | O |  |  |  | O |  | O | O |  |  |  |
| 64 |  | O | O | O | O | O | O |  |  | O |  | O |  |  | O |  |
| 65 | O |  |  |  |  |  |  |  | O |  |  |  |  |  |  |  |
| 66 | O |  |  |  |  |  | O |  | O |  |  |  |  |  | O |  |
| 67 | O |  |  |  |  | O |  |  | O |  |  |  |  | 0 |  |  |
| 68 | O |  |  |  |  | O | O |  | O |  |  |  |  |  | O |  |

Prop: Proportional     Cond: Condensed     H.Q.: High Quality     D.S.: Double Strike     Sup/Sub: Superscript/Subscript

|  | Command Combination | Character Mode Printed | Printed Ex. |
| --- | --- | --- | --- |
| No. | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | Pica | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | ABChijk |
| 69 | O |  |  |  | O |  |  |  | O |  |  |  | O |  |  |  |
| 70 | O |  |  |  | O |  | O |  | O |  |  |  |  |  | O |  |
| 71 | O |  |  |  | O | O |  |  | O |  |  |  | O |  |  |  |
| 72 | O |  |  |  | O | O | O |  | O |  |  |  |  |  | O |  |
| 73 | O |  |  | O |  |  |  |  | O |  |  | O |  |  |  |  |
| 74 | O |  |  | O |  |  | O |  | O |  |  | O |  |  | O |  |
| 75 | O |  |  | O |  | O |  |  | O |  |  | O |  | O |  |  |
| 76 | O |  |  | O |  | O | O |  | O |  |  | O |  |  | O |  |
| 77 | O |  |  | O | O |  |  |  | O |  |  | O | O |  |  |  |
| 78 | O |  |  | O | O |  | O |  | O |  |  | O |  |  | O |  |
| 79 | O |  |  | O | O | O |  |  | O |  |  | O | O |  |  |  |
| 80 | O |  |  | O | O | O | O |  | O |  |  | O |  |  | O |  |
| 81 | O |  | O |  |  |  |  |  | O |  |  |  |  |  |  |  |
| 82 | O |  | O |  |  |  | O |  | O |  |  |  |  |  | O |  |
| 83 | O |  | O |  |  | O |  |  | O |  |  |  |  | O |  |  |
| 84 | O |  | O |  |  | O | O |  | O |  |  |  |  |  | O |  |
| 85 | O |  | O |  | O |  |  |  | O |  |  |  | O |  |  |  |
| 86 | O |  | O |  | O |  | O |  | O |  |  |  |  |  | O |  |
| 87 | O |  | O |  | O | O |  |  | O |  |  |  | O |  |  |  |
| 88 | O |  | O |  | O | O | O |  | O |  |  |  |  |  | O |  |
| 89 | O |  | O | O |  |  |  |  | O |  |  | O |  |  |  |  |
| 90 | O |  | O | O |  |  | O |  | O |  |  | O |  |  | O |  |
| 91 | O |  | O | O |  | O |  |  | O |  |  | O |  | O |  |  |
| 92 | O |  | O | O |  | O | O |  | O |  |  | O |  |  | O |  |
| 93 | O |  | O | O | O |  |  |  | O |  |  | O | O |  |  |  |
| 94 | O |  | O | O | O |  | O |  | O |  |  | O |  |  | O |  |
| 95 | O |  | O | O | O | O |  |  | O |  |  | O | O |  |  |  |
| 96 | O |  | O | O | O | O | O |  | O |  |  | O |  |  | O |  |
| 97 | O | O |  |  |  |  |  |  | O |  |  |  |  |  |  |  |
| 98 | O | O |  |  |  |  | O |  | O |  |  |  |  |  | O |  |
| 99 | O | O |  |  |  | O |  |  | O |  |  |  |  | O |  |  |
| 100 | O | O |  |  |  | O | O |  | O |  |  |  |  |  | O |  |
| 101 | O | O |  |  | O |  |  |  | O |  |  |  | O |  |  |  |
| 102 | O | O |  |  | O |  | O |  | O |  |  |  |  |  | O |  |

Prop: Proportional     Cond: Condensed     H.Q.: High Quality     D.S.: Double Strike     Sup/Sub: Superscript/Subscript

|  | Command Combination | Character Mode Printed | Printed Ex. |
| --- | --- | --- | --- |
| No. | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | Pica | Elite | Prop | Cond | Bold | H.Q. | D.S. | Sup/Sub | ABChijk |
| 103 | O | O |  |  | O | O |  |  | O |  |  |  | O |  |  |  |
| 104 | O | O |  |  | O | O | O |  | O |  |  |  |  |  | O |  |
| 105 | O | O |  | O |  |  |  |  | O |  |  | O |  |  |  |  |
| 106 | O | O |  | O |  |  | O |  | O |  |  | O |  |  | O |  |
| 107 | O | O |  | O |  | O |  |  | O |  |  | O |  | O |  |  |
| 108 | O | O |  | O |  | O | O |  | O |  |  | O |  |  | O |  |
| 109 | O | O |  | O | O |  |  |  | O |  |  | O | O |  |  |  |
| 110 | O | O |  | O | O |  | O |  | O |  |  | O |  |  | O |  |
| 111 | O | O |  | O | O | O |  |  | O |  |  | O | O |  |  |  |
| 112 | O | O |  | O | O | O | O |  | O |  |  | O |  |  | O |  |
| 113 | O | O | O |  |  |  |  |  | O |  |  |  |  |  |  |  |
| 114 | O | O | O |  |  |  | O |  | O |  |  |  |  |  | O |  |
| 115 | O | O | O |  |  | O |  |  | O |  |  |  |  | O |  |  |
| 116 | O | O | O |  |  | O | O |  | O |  |  |  |  |  | O |  |
| 117 | O | O | O |  | O |  |  |  | O |  |  |  | O |  |  |  |
| 118 | O | O | O |  | O |  | O |  | O |  |  |  |  |  | O |  |
| 119 | O | O | O |  | O | O |  |  | O |  |  |  | O |  |  |  |
| 120 | O | O | O |  | O | O | O |  | O |  |  |  |  |  | O |  |
| 121 | O | O | O | O |  |  |  |  | O |  |  | O |  |  |  |  |
| 122 | O | O | O | O |  |  | O |  | O |  |  | O |  |  | O |  |
| 123 | O | O | O | O |  | O |  |  | O |  |  | O |  | O |  |  |
| 124 | O | O | O | O |  | O | O |  | O |  |  | O |  |  | O |  |
| 125 | O | O | O | O | O |  |  |  | O |  |  | O | O |  |  |  |
| 126 | O | O | O | O | O |  | O |  | O |  |  | O |  |  | O |  |
| 127 | O | O | O | O | O | O |  |  | O |  |  | O | O |  |  |  |
| 128 | O | O | O | O | O | O | O |  | O |  |  | O |  |  | O |  |

# _APPENDIX C (Character Category Specifications)_____________

| Number of Passes | 1 | 1 | 1 | 2 | 2 | 1 | 1 | 1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | “*” Includes Half Dot Note: Print speeds (CPS) of 2-pass mode shown here exclude a return time of the print head between the first and the second pass |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Character Dimensions (H x V in mm) | 2.0 x 2.5 (*9 x 7) | 1.8 x 2.5 (*9 x 7) | 1.2 x 2.5 (*9 x 7) | 2.3 x 2.5 (*19 x 13) | 1.9 x 2.5 (*19 x 13) | 2.7 x 2.5 | 2.3 x 2.5 | 1.5 x 2.5 | 2.9 x 2.5 | 2.5 x 2.5 | - | - | - | - | - | - | - |  |
| Minimum Dot Spacing (H x V in inches) | 1/120* x 1/72 | 1/144* x 1/72 | 1/240* x 1/72 | 1/240* x 1/144 | 1/288* x 1/144 | 1/240* x 1/72 | 1/288* x 1/72 | 1/480* x 1/72 | 1/480* x 1/144 | 1/576* x 1/144 | 1/60 x 1/72 | 1/120 x 1/72 | 1/120* x 1/72 | 1/240* x 1/72 | 1/80 x 1/72 | 1/72 x 1/72 | 1/90 x 1/72 |  |
| Print Speed (CPS) | 80 | 96 | 68.5 | 20 | 24 | 80 | 96 | 68.5 | 20 | 24 | 480 dot column/s | 480 dot column/s | *960 dot column/s | *960 dot column/s | 320 dot column/s | 576 dot column/s | 360 dot column/s |  |
| Character Spacing (CPI) | 10 | 12 | 17 | 10 | 12 | 10 | 12 | 17 | 10 | 12 | - | - | - | - | - | - | - |  |
| Maximum Column Number | 80 | 96 | 137 | 80 | 96 | 80 | 96 | 137 | 80 | 96 | 480 dot column | 960 dot column | *960 dot column | *1920 dot column | 640 dot column | 576 dot column | 720 dot column |  |
| Character Structure (H x V + Space) | 12* x 9 | 12* x 9 | 14* x 9 | 24* x 18 | 24* x 18 | 16* x 9 | 16* x 9 | 18* x 9 | 32* x 18 | 32* x 18 | n x 8 | n x 8 | n x 8 | n x 8 | n x 8 | n x 8 | n x 8 |  |
| Character Category | Pica | Elite | Condensed | Pica | Elite | Pica | Elite | Condensed | Pica | Elite | Standard Density Graphic | Double Density Graphic | Double-Speed Double-Density Graphic | Quadruple Density Graphic | 640 Dot Graphic | 576 Dot Graphic | 720 Dot Graphic |  |
|  | Standard | High Quality (N.L.Q) | Standard | High Quality (N.L.Q) |  |  |  |  |  |  |  |  |
|  | Standard Character | Italic Cursive Characters | Graphic |  |

# _APPENDIX D (Control Code Summary)______________________

| Category | Item | Symbol | Hex (Decimal) Code | Function | Page |
| --- | --- | --- | --- | --- | --- |
| Print Command | 1 | CR | 0D (13) | Printing only or plus linefeed | 21 |
|  | 2 | NL | 0A (10) | New line after printing | 21 |
|  | 3 | FF | OC (12) | Form feed after printing | 22 |
|  | 4 | VT | 0B (11) | Same as NL | 22 |
|  | 5 | ESC,J,n | 1B, 4A, n (27, 74, n) | n/216 “ linefeed after printing | 23 |
| Character Mode Designation | 6 | ESC,P | 1B, 50 (27, 80) | Elite character mode termination | 23 |
|  | 7 | ESC,M | 1B, 4D (27, 77) | Elite character mode designation | 23 |
|  | 8 | SI | 0F (15) | Condensed character mode designation | 24 |
|  | 9 | ESC,SI | 1B, 0F (27, 15) | Same as SI | 24 |
|  | 10 | DC2 | 12 (18) | Condensed character mode termination | 24 |
|  | 11 | ESC,x,(01) | 1B, 78, 01 (27, 120, 1) | High Quality character mode designation | 25 |
|  | 12 | ESC,x,(00) | 1B, 78, 00 (27, 120, 0) | High quality character mode termination | 25 |
|  | 13 | ESC,p,(01) | 1B, 70, 01 (27, 112, 1) | Proportional character mode designation | 26 |
|  | 14 | ESC,p,(00) | 1B, 70, 00 (27, 112, 0) | Proportional character mode termination | 26 |
|  | 15 | ESC,S,(00) | 1B, 53, 00 (27, 83, 0) | Superscript character mode designation | 27 |
|  | 16 | ESC,S,(01) | 1B, 53, 01 (27, 83, 1) | Subscript character mode designation | 27 |
|  | 17 | ESC,T | 1B, 54 (27, 84) | Subscript/Superscript character mode termination | 28 |
|  | 18 | ESC,4 | 1B, 34 (27, 52) | Italic character mode designation | 28 |
|  | 19 | ESC,5 | 1B, 35 (27,53) | Italic character mode termination | 29 |
|  | 20 | ESC,!,n | 1B, 21, n (27, 33, n) | Combined print mode designation | 29 |
| Bold Character | 21 | ESC,E | 1B, 45 (27,69) | Bold character mode designation | 32 |
|  | 22 | ESC,F | 1B, 46 (27,70) | Bold character mode termination | 32 |
| Double Strike Character Mode | 23 | ESC,G | 1B, 47 (27,71) | Double Strike character mode designation | 33 |
|  | 24 | ESC,H | 1B, 48 (27,72) | Double Strike character mode termination | 33 |
| Double Width Character Mode | 25 | SO | 0E (14) | Double width character mode designation (line feed terminates the command) | 34 |
|  | 26 | ESC,SO | 1B, 0E (27,14) | Same as SO | 34 |
|  | 27 | DC4 | 14 (20) | Termination of the SO command | 34 |
|  | 28 | ESC,W,(01) | 1B, 57, 01 (27, 87, 1) | Double Width character mode designation (line feed does not terminate the command) | 35 |
|  | 29 | ESC,W,(00) | 1B, 57, 00 (27, 87, 0) | ESC, W, (01) command termination | 35 |

| Category | Item | Symbol | Hex (Decimal) Code | Function | Page |
| --- | --- | --- | --- | --- | --- |
| Graphic Print Mode | 30 | ESC, K, n1, n2 | 1B, 4B, n1, n2 (27, 75, n1, n2) | Standard density graphic designation | 36 |
|  | 31 | ESC, L, n1, n2 | 1B, 4C, n1, n2 (27, 76, n1, n2) | Double density graphic designation | 37 |
|  | 32 | ESC, Y, n1, n2 | 1B, 59, n1, n2 (27, 89, n1, n2) | Double-speed double density graphic designation | 38 |
|  | 33 | ESC, Z, n1, n2 | 1B, 5A, n1, n2 (27, 90, n1, n2) | Quadruple density graphic designation | 39 |
|  | 34 | ESC, *, m, n1, n2 | 1B, 2A, m, n1, n2 (27, 42, m, n1, n2) | Various graphic modes designation | 40 |
|  | 35 | ESC, ^, a, n1. n2 | 1B, 5E, a, n1, n2 (27, 94, a, n1, n2) | 9-pin graphic designation | 41 |
| Line Feed Spacing | 36 | ESC, 0 | 1B, 30 (27, 48) | Set line feed pitch to 1/8” | 42 |
|  | 37 | ESC, 1 | 1B, 31 (27, 49) | Set line feed pitch to 7/72” | 42 |
|  | 38 | ESC, 2 | 1B, 32 (27, 50) | Set line feed pitch to 1/6” | 43 |
|  | 39 | ESC, 3, n | 1B, 33, n (27, 51, n) | Set line feed pitch to n/216” | 43 |
|  | 40 | ESC, A, n | 1B, 41, n (27, 65, n) | Set line feed pitch to n/72” | 44 |
| Page Length Setting | 41 | ESC, C, n | 1B, 43, n (27, 67, n) | Line unit page length setting | 45 |
|  | 42 | ESC, C, (00), n | 1B, 43, 00, n (27, 67,0, n) | Inch unit page length setting | 46 |
| Horizontal Tab | 43 | ESC, D, n1, n2, …,nk, NUL | 1B, 44, n1, n2, …nk,00 (27, 68, n1, n2, …nk, 0) | Horizontal tab position setting | 47 |
|  | 44 | HT | 09 (9) | Move to next horizontal tab position | 48 |
| Margin Setting | 45 | ESC, Q, n | 1B, 51, n (27, 81, n) | Right margin setting | 48 |
|  | 46 | ESC, l, n | 1B, 6C, n (27, 108, n) | Left margin setting | 49 |
| Underline | 47 | ESC, -, (01) | 1B, 2D, 01 (27, 45, 1) | Underline setting | 50 |
|  | 48 | ESC, -, (00) | 1B, 2D, 00 (27, 45, 0) | Underline termination | 50 |
| Buffer Clear | 49 | CAN | 18 (24) | Clearing of internal buffer | 51 |
| Backspace | 50 | BS | 08 (8) | After printing, move 1 character position to the left | 51 |
| Buzzer | 51 | BEL | 07 (7) | Sound buzzer for 0.3 seconds | 52 |
| Home Positioning | 52 | ESC, < | 1B, 3C (27,60) | Move print head to home position | 52 |
| Skip-Over Perforation | 53 | ESC, N, n | 1B, 4E, n (27, 78, n) | Skip over n bottom lines of the page | 53 |
|  | 54 | ESC, O | 1B, 4F (27, 69) | Termination of skip over perforation | 54 |
| Paper Out Detection | 55 | ESC, 8 | 1B, 38 (27, 56) | Ignore paper out detection | 54 |
|  | 56 | ESC, 9 | 1B, 39 (27,57) | Make paper out detection valid | 54 |
| Reset | 57 | ESC, @ | 1B, 40 (27, 64) | Initialise printer | 54 |
| Unidirectional Printing | 58 | ESC, U, (01) | 1B, 55, 01 (27, 85, 1) | Unidirectional printing designation | 55 |
|  | 59 | ESC, U, (00) | 1B, 55, 00 (27, 85, 0) | Bidirectional printing designation | 55 |

8503 – 65A01